## Slide 1: Dr. Yifeng Zhu Electrical and Computer Engineering University of Maine
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 16
General-purpose Timers

## Slide 2: Input Capture
Capture the timestamp of the occurrence of a rising or a falling edge transition in a digital signal

## Slide 3
0
ARR=99
30
63
External signal
Hardware copies counter to CCR, thus CCR = 30
Hardware generates an interrupt to run timer ISR()
Hardware copies counter to CCR, thus CCR = 63
Hardware generates an interrupt to run timer ISR()
Time span between two events = 63 – 30 = 33 time units

## Slide 4: Input Capture
Record the timestamp of an external event
Capture both rising and falling edges
Measuring low or high time
External Signal 1
External Signal 2
time

## Slide 5: Input Capture
Capture only rising edges or only falling edges
Measuring the period
External Signal 1
External Signal 2
time

## Slide 6: Input Capture
Latch the counter value into CCR after a transition is detected
If enabled, generate an interrupt to inform the processor to read CCR
Hold in CCR
(Capture/Compare register)

## Slide 7
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
0
1
2
3
4
5
6
Timer: Upcounting mode, ARR = 6
Clock
Counter
Timer
Counter
fCL_PSC
PSC
Prescaler
fCL_CNT
clock
Counter is incremented/decremented once per cycle.
Notes: A single timer can generate up to 4 PWM signals with independent duty cycles and identical frequency. When multiple PWM signals are generated by the same timer, all rising edges occur at the same time. That is why it is called edge-aligned.

## Slide 8
External Input Signal
CCRnew
CCRold
0
ARR
ARR
Timer
Counter
0
Capture only rising edges

## Slide 9: Input Filtering
Digital filter for debouncing and noise removal
  N consecutive samples with the new level
Filter acceptance = 2

## Slide 10: Input Prescaler
Assume capture only rising edge
External Signal
Capture every rising edge
Capture every 2 rising edges
Capture every 4 rising edges

## Slide 11: Input Capture Diagram

## Slide 12: Quiz: Input Capture
How does software know a capture event occur?
via interrupt

## Slide 13: Recall: Enable an Interrupt
Peripheral
ARM Cortex-M
Execution
Core
NVIC
Interrupt Request
Interrupt Request
Nested Vectored Interrupt Controller
Two steps:
Program the peripheral control register to allow it to generate interrupts
Program NVIC to allow it to accept interrupts

## Slide 14: Timer DMA/Interrupt Enable Register (DIER)
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
... | TIE | COMIE | CC4IE | CC3IE | CC2IE | CC1IE | UIE
…
UIE: Update Interrupt Enable
CC1IE: Capture/compare Channel 1 Interrupt Enable
CC2IE: Capture/compare Channel 2 Interrupt Enable
CC3IE: Capture/compare Channel 3 Interrupt Enable
CC4IE: Capture/compare Channel 4 Interrupt Enable
TIE: Trigger Interrupt Enable
...
1 = enable, 0 = disable

## Slide 15: Timer DMA/Interrupt Enable Register (DIER)
8 | 6 | 5 | 4 | 3 | 2 | 1 | 0
BIE | TIE | COMIE | CC4IE | CC3IE | CC2IE | CC1IE | UIE
…
Enable interrupt
TIM4->DIER |= 0x02; // Enable interrupt for channel 1
NVIC_EnableIRQ(TIM4_IRQn); // Enable interrupt for timer 4
Disable interrupt
TIM4->DIER &= ~0x02; // Disable interrupt for channel 1
NVIC_DisableIRQ(TIM4_IRQn); // Disable interrupt for timer 4
1 = enable, 0 = disable

## Slide 16: Find out the interrupt event
For a timer, multiple events can trigger an interrupt
How does the software know which event has trigger the interrupt?
OR Gate
channel 1 interrupt
timer interrupt
channel 2 interrupt
channel 3 interrupt
channel 4 interrupt
counter update (counter overflow or underflow)

## Slide 17: Find out the interrupt event
void TIM4_IRQHandler (void) {
if(TIM4->SR & TIM_SR_UIF) { // UIF Interrupt
...
} else if (TIM4->SR & TIM_SR_CC1IF) { // Channel #1
...
} else if (TIM4->SR & TIM_SR_CC2IF) { // Channel #2
...
}
...
}

## Slide 18: Find out the interrupt event
void TIM4_IRQHandler (void) {
if(TIM4->SR & TIM_SR_UIF) { // UIF Interrupt
TIM4->SR &= ~TIM_SR_UIF; // Clear interrupt flag
...
} else if (TIM4->SR & TIM_SR_CC1IF) { // Channel #1
TIM4->SR &= ~ TIM_SR_CC1IF; // Clear interrupt flag
...
} else if (TIM4->SR & TIM_SR_CC2IF) { // Channel #2
TIM4->SR &= ~ TIM_SR_CC2IF; // Clear interrupt flag
...
}
...
}
Hardware sets these flags, and software needs to clear them.

## Slide 19: Timer Status Register (SR)
8 | 6 | 5 | 4 | 3 | 2 | 1 | 0
BIF | TIF | COMIF | CC4IF | CC3IF | CC2IF | CC1IF | UIF
TIMx_SR = 0 (default)
UIF is set by hardware and needs to be cleared by software.
if (TIM4->SR & 0x01 == 0x01) { // Test UIF
// If hardware sets UIF, do some actions
...
// Clear UIF
TIM4->SR &= ~0x01;
}
…

## Slide 20: Timer Status Register (SR)
8 | 6 | 5 | 4 | 3 | 2 | 1 | 0
BIF | TIF | COMIF | CC4IF | CC3IF | CC2IF | CC1IF | UIF
TIMx_SR = 0 (default)
CC1IF: Capture/Compare 1 interrupt flag
…
If channel CC1 is configured as output, this flag is set by hardware when the counter matches the compare value, with some exception in center-aligned mode. It is cleared by software.
0: No match.
1: The content of the counter TIMx_CNT matches the content of the TIMx_CCR1 register.
When the contents of TIMx_CCR1 are greater than the contents of TIMx_ARR, the CC1IF bit goes high on the counter overflow (in upcounting and up/down-counting modes) or underflow (in downcounting mode)

## Slide 21: Timer Status Register (SR)
8 | 6 | 5 | 4 | 3 | 2 | 1 | 0
BIF | TIF | COMIF | CC4IF | CC3IF | CC2IF | CC1IF | UIF
TIMx_SR = 0 (default)
CC1IF: Capture/Compare 1 interrupt flag
…
If channel CC1 is configured as input, this bit is set by hardware on a capture. It is cleared by software or by reading the TIMx_CCR1 register.
0: No input capture occurred
1: The counter value has been captured in TIMx_CCR1 register (An edge has been detected on IC1 which matches the selected polar

## Slide 22: Channel 1 for Input Capture
Define the frequency and the length of sampling
e.g. 1000: fSAMPLING = fDTS/8, N = 6
CC1NP/CC1P
00, noninverted/rising edge
01: inverted/falling edge
10: reserved
11: noninverted/both edges
IC1PSC[1:0]
e.g. capture is done once every 4 events

## Slide 23: Ultrasonic Distance Sensor

## Slide 24: Ultrasonic Distance Sensor
The echo pulse width corresponds to round-trip time.
or
If pulse width is 38ms, no obstacle is detected.

## Slide 25: Ultrasonic Distance Sensor