## Slide 1: Z. Gu
Fall 2025
Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C
Chapter 6
Control Flow in Assembly
Acknowledgement: Lecture slides based on Embedded Systems with ARM Cortex-M Microcontrollers in Assembly Language and C, University of Maine https://web.eece.maine.edu/~zhu/book/

## Slide 2: Three Control Structures
Sequence Structure
  Computer executes statements (instructions), one after another, in the order listed in the program
Selection Structure
  If-then-else
Loop Structure
  while loop
  for loop
Sequence Structure
Selection Structure
Loop Structure

## Slide 3: Combined Program Status Registers (xPSR)
Review
Notes: The Q flag is sticky in that, when set to 1 by an instruction, it remains set until explicitly cleared to 0 by an MSR instruction writing to the CPSR. Instructions cannot execute conditionally on the status of the Q flag.
Saturation arithmetic is a version of arithmetic in which all operations such as addition and multiplication are limited to a fixed range between a minimum and maximum value. If the result of an operation is greater than the maximum it is set ("clamped") to the maximum, while if it is below the minimum it is clamped to the minimum. The name comes from how the value becomes "saturated" once it reaches the extreme values; further additions to a maximum or subtractions from a minimum will not change the result.
For example, if the valid range of values is from -100 to 100, the following operations produce the following values:
60 + 43 = 100
(60 + 43) − 150 = −50
43 − 150 = −100
60 + (43 − 150) = −40
10 × 11 = 100
99 × 99 = 100
30 × (5 − 1) = 100
30×5 − 30×1 = 70
Green psr bits are only in certain versions of the ARM architecture
ALU status flags (set if "S" bit set, implied in Thumb state).
Sticky overflow flag (Q flag) is set either when
  saturation occurs during QADD, QDADD, QSUB or QDSUB, or
  the result of SMLAxy or SMLAWx overflows 32-bits
Once flag has been set can not be modified by one of the above instructions and must write to CPSR using MSR instruction to cleared
PSRs split into four 8-bit fields that can be individually written:
Control (c) bits 0-7
Extension (x) bits 8-15 Reserved for future use
Status (s) bits 16-23 Reserved for future use
Flags (f) bits 24-31
Bits that are reserved for future use should not be modified by current software. Typically, a read-modify-write strategy should be used to update the value of a status register to ensure future compatibility. Note that the T/J bits in the CPSR should never be changed directly by writing to the PSR (use the BX/BXJ instruction to change state instead).
However, in cases where the processor state is known in advance (e.g. on reset, following an interrupt, or some other exception), an immediate value may be written directly into the status registers, to change only specific bits (e.g. to change mode).
New ARM V6 bits now shown.

## Slide 4: Condition Flags
Negative bit
  N = 1 if most significant bit of result is 1
Zero bit
  Z = 1 if all bits of result are 0
Carry bit
  For unsigned addition, C = 1 if carry takes place
  For unsigned subtraction, C = 0 (carry = not borrow) if borrow takes place
  For shift/rotation, C = last bit shifted out
oVerflow bit
  V = 1 if adding 2 same-signed numbers produces a result with the opposite sign
    Positive + Positive = Negative, or
    Negative + negative = Positive
  Non-arithmetic operations does not touch V bit, such as MOV,AND,LSL,MUL
Reserved
ISR number
Program Status Register (PSR)
ICI/IT
T
N
Z
C
V
Q
ICI/IT
GE
Reserved
Review
Notes: N (negative) – set (1) when a signed result is negative, otherwise cleared (0).
Z (zero) – set (1) when a result is 0, otherwise cleared (0).
C (carry) – set (1) when an add-based operation produces an overflow, when a subtract-based operation doesn’t require a borrow; when shifting, holds the last bit that’s been shifted out; otherwise cleared (0).
V (overflow) – set (1) when an add- or subtract-based operation generates a signed overflow, otherwise cleared (0).

## Slide 5: Carry and Overflow Flags w/ Arithmetic Instructions
5
Carry flag C = 1 (Borrow flag = 0) upon an unsigned addition if the answer is wrong (true result > 2n-1)
Carry flag C = 0 (Borrow flag = 1) upon an unsigned subtraction if the answer is wrong (true result < 0)
Overflow flag V =1 upon a signed addition or subtraction if the answer is wrong (true result > 2n-1-1 or true result < -2n-1)
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs; Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
 | Unsigned Addition | Unsigned Subtraction | Signed Addition or Subtraction
Carry flag | true result > 2n-1  Carry flag=1 Borrow flag=0 (Result incorrect) | true result < 0  Carry flag=0 Borrow flag=1 (Result incorrect) | N/A
Overflow flag | N/A | N/A | true result > 2n-1-1 or true result < -2n-1 Overflow flag=1 (Result incorrect)
Review
Notes: C is cleared upon an unsigned subtract if the answer is wrong
The carry flag (CF) is set differently for unsigned addition and subtraction:
When adding or subtracting two signed numbers in an n-bit system, an overflow occurs if the true result is larger than the maximum signed integer (i.e. ) or smaller than the minimum signed integer (i.e. ) that can be represented
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs, including:
  adding two positive numbers
  adding two negative numbers
  subtracting a positive number from a negative number
  subtracting a negative number from a positive number
Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
  Why?
Unsigned Addition:
The carry flag is set to 1 if there is a carry out from the most significant bit (MSB) during the addition.
This means the sum exceeds the maximum value that can be represented in the given number of bits.
Example: Adding two 8-bit numbers resulting in a value greater than 255 will set CF = 1.
Unsigned Subtraction:
The carry flag acts as a borrow indicator for subtraction.
CF is cleared (set to 0) if a borrow is needed (i.e., if the minuend is less than the subtrahend).
CF is set to 1 if no borrow is needed, meaning the subtraction did not underflow.
Summary:
For unsigned addition, CF = 1 means an overflow beyond the MSB (carry out).
For unsigned subtraction, CF = 0 means a borrow (underflow), CF = 1 means no borrow.
The carry flag thus helps detect unsigned overflow or underflow conditions.
This behavior contrasts with signed arithmetic, where the overflow flag (OF) signals signed overflow, and the carry flag is generally not used.
References from teaching and documentation explain this clearly: The carry flag signals actual carry for addition and borrow for subtraction in unsigned arithmetic scenarios.
C is cleared upon an unsigned subtract if the answer is wrong
The carry flag (CF) is set differently for unsigned addition and subtraction:
When adding or subtracting two signed numbers in an n-bit system, an overflow occurs if the true result is larger than the maximum signed integer (i.e. 2^(𝑛−1)−1) or smaller than the minimum signed integer (i.e. 〖−2〗^(𝑛−1)) that can be represented
Overflow may occur when adding 2 operands with the same sign, or subtracting 2 operands with different signs, including:
  adding two positive numbers
  adding two negative numbers
  subtracting a positive number from a negative number
  subtracting a negative number from a positive number
Overflow cannot occur when adding 2 operands with different signs or when subtracting 2 operands with the same sign.
  Why?
Unsigned Addition:
The carry flag is set to 1 if there is a carry out from the most significant bit (MSB) during the addition.
This means the sum exceeds the maximum value that can be represented in the given number of bits.
Example: Adding two 8-bit numbers resulting in a value greater than 255 will set CF = 1.
Unsigned Subtraction:
The carry flag acts as a borrow indicator for subtraction.
CF is cleared (set to 0) if a borrow is needed (i.e., if the minuend is less than the subtrahend).
CF is set to 1 if no borrow is needed, meaning the subtraction did not underflow.
Summary:
For unsigned addition, CF = 1 means an overflow beyond the MSB (carry out).
For unsigned subtraction, CF = 0 means a borrow (underflow), CF = 1 means no borrow.
The carry flag thus helps detect unsigned overflow or underflow conditions.
This behavior contrasts with signed arithmetic, where the overflow flag (OF) signals signed overflow, and the carry flag is generally not used.
References from teaching and documentation explain this clearly: The carry flag signals actual carry for addition and borrow for subtraction in unsigned arithmetic scenarios.

## Slide 6: Updating Condition Flags
Method 1: append “S”: updates destination register, and sets flags
  ADD r0,r1,r2 → ADDS r0,r1,r2
  SUB r0,r1,r2 → SUBS r0,r1,r2
  Performs operation, writes the result into Rd, and also updates NZCV flags
Method 2: compare instructions: sets flags only
  CMP/CMN/TEQ/TST: performs operation to update NZCV flags, but the computation result is not saved and discarded
Notes: it’s a “compare-only” operation for branching or predication.
; it both computes and compares in one step
Flag Setting Instructions:
CMP: R1 - R2 (result discarded)
TST: R1 & R2 (result discarded)
TEQ: R1 ⊕ R2 (result discarded)
CMN: R1 + R2 (result discarded)

## Slide 7: Updating Condition Flags
Update flags
  No need to add S. No need to specify destination register.
Operations are:
  CMP R1 – R2: Same as SUBS, except result discarded (not written to destination register)
  CMN R1 + R2: Same as ADDS, except result discarded
  TST R1 & R2: Same as ANDS, except result discarded
  TEQ R1 ⊕ R2: Same as EORS, except result discarded
Examples:
  CMP r0, r1
  TST r2, #5
Instruction | Operands | Brief description | Flags
CMP | R1 - R2 | Compare | N,Z,C,V
CMN | R1 + R2 | Compare Negative | N,Z,C,V
TST | R1 & R2 | Test | N,Z,C
TEQ | R1 ⊕ R2 | Test Equivalence | N,Z,C
Notes: SUBS Rd, R1, R2: performs subtraction , writes the result into Rd, and also updates NZCV flags; it both computes and compares in one step.
CMP/CMN/TEQ/TST: performs operations to update NZCV flags, but the computation result is not saved and discarded; it’s a “compare-only” operation for branching or predication.
CMP R1, R2
CMN R1, R2
Update N, Z, C and V according to the result
CMP subtracts R2 from R1.
  Same as SUBS, except result is discarded.
CMN adds R2 to R1.
  Same as ADDS, except result is discarded.
SUBS Rd, Rn, Op2: performs subtraction 𝑅𝑛 − 𝑂𝑝2, writes the result into Rd, and also updates NZCV flags; it both computes and compares in one step.
CMP/CMN/TEQ/TST: performs operations to update NZCV flags, but the computation result is not saved and discarded; it’s a “compare-only” operation for branching or predication.
CMP Rn, Op2
CMN Rn, Op2
Update N, Z, C and V according to the result
CMP subtracts Op2 from Rn.
  Same as SUBS, except result is discarded.
CMN adds Op2 to Rn.
  Same as ADDS, except result is discarded.

## Slide 8: Example of CMP
Area absolute, CODE, READONLY
EXPORT __main
ENTRY
__main PROC
CMP r1, #0 ; r1 = x
RSBLT r0, r1, #0
done B done ; deadloop, end of program
ENDP
END
RSBLT r0, r1, #0:: conditional execution of the RSB instruction with condition code LT. If r1 < 0, then set r0 = 0 − r1 = -r1
Notes: Note: RSB = Reverse SuBtract

## Slide 9: Updating Condition Flags: TST and TEQ
TST R1, R2 ; Bitwise AND
TEQ R1, R2 ; Bitwise Exclusive OR
Update N and Z according to the result
Can update C during the calculation of R2 (w/ shifting such as LSL, LSR…)
Do not affect V
TST performs bitwise AND on R1 and R2.
  Same as ANDS, except result discarded.
  Use R2 as a mask; Z=0 implies “some masked bit(s) are set, so result is non-zero” Z=1 implies “none of the masked bit(s) are set, so result is zero.” For a single-bit mask, Z=0 means “that bit in R1 is 1,” and Z=1 means “that bit is 0.”
TEQ performs bitwise Exclusive OR on R1 and R2.
  Same as EORS, except result discarded.
  If R1 and R2 are equal, then R1 R2 is 0, and Z is set to 1; otherwise Z is set to 0 (cleared).
x | y | x AND y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | x XOR y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Notes: It computes logical operation internally, writes no result to a register, and updates the condition flags based on that XOR.
If is 0x0, then R1 and R2 are equal, Z is set to 1; otherwise Z is cleared.
It computes logical operation 𝑅𝑑⊕𝑂𝑝 internally, writes no result to a register, and updates the condition flags based on that XOR.
If 𝑅𝑛" ∧ " 𝑂𝑝𝑒𝑟𝑎𝑛𝑑2 is 0x0, then Rn and Op2 are equal, Z is set to 1; otherwise Z is cleared.

## Slide 10: Example of TEQ
Translate C code into assembly:
TEQ r0, #‘!’ performs a test-equal by computing r0 - ‘!’ and setting condition flags; Z=1 when r0 equals ‘!’.
TEQNE r0, #‘?’ executes only if the previous Z=0 (i.e., char was not ‘!’); it tests r0 against ‘?’ and sets Z accordingly. This achieves the logical OR without branches by conditionally running the second test only when needed.
  Logical OR operator (||) employs short-circuit evaluation, meaning it evaluates expressions from left to right and stops as soon as the result of the entire expression is determined. For (cond1||cond2): If cond1 evaluates to true (non-zero), the overall result of the || operation is already known to be true, so cond2 is not evaluated. If cond1 evaluates to false (zero), the evaluation proceeds to the next operand cond2.
ADDEQ r1, r1, #1 executes only if Z=1 after the tests, meaning char matched either ‘!’ or ‘?’.
  If r0 == ‘!’, then TEQ sets Z = 1. TEQNE is skipped, and ADDEQ is executed
  The 2nd TEQNE executes only if the first comparison failed (Z=0). If r0 == ‘?’, then TEQNE is executed and sets Z = 1, and ADDEQ is executed
  If r0 != ‘!’ && r0 != ‘?’, then TEQ sets Z = 0, TEQNE is executed and sets Z = 0, and ADDEQ is not executed
C Code | Assembly
if (char==‘!’¦¦char==‘?’) found++; | TEQ r0, #‘!’ TEQNE r0, #‘?’ ADDEQ r1, r1, #1

## Slide 11: Unconditional Branch Instructions
B label or BAL label
  cause a branch to label.
BL label
  copy the address of the next instruction into r14 (lr, the link register), and
  cause a branch to label.
BX Rm
  branch to the address held in Rm
BLX Rm:
  copy the address of the next instruction into r14 (lr, the link register) and
  branch to the address held in Rm
Instruction | Operands | Brief description
B, BAL | label | Branch
BL | label | Branch with Link
BLX | Rm | Branch indirect with Link
BX | Rm | Branch indirect

## Slide 12: Unconditional Branch Instructions: A Simple Example
A label marks the location of an instruction
Labels help human to read the code
In machine program, labels are converted to numeric offsets by assembler
Here MOVS can be replaced by MOV since the flags are not used
MOVS r1, #1
B target ; Branch to target
MOVS r2, #2 ; Not executed
MOVS r3, #3 ; Not executed
MOVS r4, #4 ; Not executed
target MOVS r5, #5

## Slide 13: Condition Codes
The possible condition codes are listed below:
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Clear
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z==0
C==1
C==0
Z==1
Flags tested
N==1
N==0
V==1
V==0
C==1 and Z==0
C==0 or Z==1
N==V
N!=V
Z==0 and N==V
Z==1 or N!=V
    Note AL is the default and does not need to be specified
CS: Carry Set
CC: Carry Clear
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 14: Signed vs. Unsigned Comparison
Op | Cond (Signed) | Flags | Explanation | Cond (Unsigned) | Flags | Explanation
R1 > R2 | GT (Greater Than) | Z=0 & N=V | Non-zero result and signs agree | HI (Higher) | C=1 & Z=0 | No borrow and not equal
R1 ≥ R2 | GE (Greater or Equal) | N=V | See next page | HS (Higher or Same) | C=1 | No borrow (R1 ≥ R2)
R1 < R2 | LT (Less Than) | N≠V | See next page | LO (Lower) | C=0 | Borrow occurred (R1 < R2)
R1 ≤ R2 | LE (Less or Equal) | Z=1 or N≠V | Zero or overflow mismatch | LS (Lower or Same) | C=0 or Z=1 | Borrow or equal
R1==R2 | EQ (Equal) |  |  |  | Z=1 | Zero
R1 ≠ R2 | NE (Not Equal) |  |  |  | Z=0 | Non-Zero
CMP R1, R2
perform subtraction R1 – R2, set flags without saving result
Notes: Key Condition Codes:
EQ/NE: Z=1 / Z=0 (Equal/Not Equal)
LT/GE: N≠V / N=V (Signed Less Than/Greater Equal)
GT/LE: Z=0 & N=V / Z=1 or N≠V (Signed Greater/Less Equal)
LO/HS: C=0 / C=1 (Unsigned Lower/Higher Same)
HI/LS: C=1 & Z=0 / C=0 or Z=1 (Unsigned Higher/Lower Same)
Flag Setting Instructions:
CMP: R1 - R2 (result discarded)
TST: R1 & R2 (result discarded)
TEQ: R1 ⊕ R2 (result discarded)
CMN: R1 + R2 (result discarded)

## Slide 15: Signed Comparison Explanations
Condition (signed) | N | V | CMP R1, R2 returns | Meaning
GE (Greater or Equal) | 0 | 0 | 1 | Result non-negative (R1 – R2 ≥ 0), no overflow → R1 ≥ R2
GE (Greater or Equal) | 1 | 1 | 1 | Result negative (R1 – R2 < 0), but overflowed so sign is flipped → true result ≥ 0 → R1 ≥ R2
LT (Less Than) | 1 | 0 | 0 | Result negative (R1 – R2 < 0), no overflow → R1 < R2
LT (Less Than) | 0 | 1 | 0 | Result non-negative (R1 – R2 ≥ 0), but overflowed so sign is flipped → true result < 0 → R1 < R2
If N = V, then GE (CMP R1, R2 returns 1)
If N ≠ V, then LT (CMP R1, R2 returns 0)

## Slide 16: Signed Comparison Examples (5-bit system)
 | N = 0 | N = 1
V = 0 | R1 = +7 (00111) R2 = +3 (00011) R1 − R2 = +4 (00100); result non‑negative and no signed overflow, so N=0, V=0 ⇒ GE holds | R1 = +3 (00011) R2 = +7 (00111) R1 − R2 = −4 (11100) result negative with no overflow, so N=1, V=0 ⇒ LT holds
V = 1 | R1 = −10 (10110) R2 = +7 (00111) R1 − R2 = −17, outside range [−16,+15]; result is 00111 (decimal 7), whose sign bit is 0 so N=0, but signed overflow occurs so V=1 ⇒ LT holds | R1 = +10 (01010) R2 = −7 (11001) R1 − R2 = +17, outside range [−16,+15]; result is 10001 (decimal −15), whose sign bit is 1 so N=1, but signed overflow occurs so V=1 ⇒ GE holds
If N = V, then GE (CMP R1, R2 returns 1)
If N ≠ V, then LT (CMP R1, R2 returns 0)
If Z=0 & N=V, then GT (result non-zero)
If Z=1 or N≠V, then LE (result may be 0)
Notes: GT (Greater Than)
Z=0 & N=V
Non-zero result and signs agree
LE (Less or Equal)
Z=1 or N≠V
In the CPSR (Current Program Status Register) of ARM processors, the N and V flags are status flags used to reflect the result of operations:
N flag (Negative flag): This flag is set to 1 if the result of an operation is negative when interpreted as a signed number. In practice, it is set to the most significant bit (bit 31) of the result. If this bit is 1, the number is negative in two's complement representation. Otherwise, it is 0.sciencedirect+1youtube
V flag (Overflow flag): This flag is set to 1 if a signed overflow has occurred in the operation—meaning the signed result does not fit in the number of bits allowed. For example, adding two large positive signed integers that produce a negative result sets V. Likewise, subtracting a large negative from a large positive can also set V. It indicates that the sign bit has been corrupted due to overflow. If no overflow occurs, V is cleared to 0.armyoutube
Together, N and V help the processor and programmers detect and handle signed arithmetic conditions like overflow and sign changes, which are critical for signed condition codes and branching decisions.
https://arm-software.github.io/CMSIS_5/Core_A/html/group__CMSIS__CPSR.html
https://www.sciencedirect.com/topics/computer-science/current-program-status-register
https://developer.arm.com/documentation/ddi0406/b/System-Level-Architecture/The-System-Level-Programmers--Model/ARM-processor-modes-and-core-registers/Program-Status-Registers--PSRs-
https://community.arm.com/arm-community-blogs/b/architectures-and-processors-blog/posts/condition-codes-1-condition-flags-and-codes
https://goiabada.github.io/docs/sections/arm-cpu/flags.html
https://heyrick.eu/assembler/psr.html
https://users.ece.utexas.edu/~valvano/EE345M/Arm_EE382N_4.pdf
https://www.youtube.com/watch?v=28MMaELXRZ0
https://azeria-labs.com/arm-conditional-execution-and-branching-part-6/
https://ece.eng.wayne.edu/~smahmud/ECECourses/ECE5620/Manuals/ARM_InstructionSet.pdf

## Slide 17: Number Interpretation
If they represent signed numbers, the latter is greater.
(1 > -1).
If they represent unsigned numbers, the former is greater
(232-1 > 1).
Which is greater?
0xFFFFFFFF or 0x00000001

## Slide 18: Which is Greater: 0xFFFFFFFF or 0x00000001?
int32_t x, y; x = -1;
y = 1; if (x > y)
...
uint32_t x, y;
x = 4294967295;
y = 1;
if (x > y)
...
BLE: Branch if less than or equal, signed ≤
BLS: Branch if lower or same, unsigned ≤
It’s software’s responsibility to tell computer how to interpret data:
If written in C, declare the signed vs unsigned variable
If written in Assembly, use signed vs unsigned branch instructions
MOV r5, #0xFFFFFFFF MOV r6, #0x00000001
CMP r5, r6 BLE Then_Clause
...
MOV r5, #0xFFFFFFFF MOV r6, #0x00000001
CMP r5, r6 BLS Then_Clause
...

## Slide 19: Conditional Branch Instructions
Conditional codes applied to branch instructions
Compare | Signed | Unsigned
> | BGT | BHI
≥ | BGE | BHS
< | BLT | BLO
≤ | BLE | BLS
== | BEQ | 
≠ | BNE | 
Compare | Signed | Unsigned
> | GT | HI
≥ | GE | HS
< | LT | LO
≤ | LE | LS
== | EQ | 
≠ | NE | 
Notes: Key Condition Codes:
EQ/NE: Z=1 / Z=0 (Equal/Not Equal)
LT/GE: N≠V / N=V (Signed Less Than/Greater Equal)
GT/LE: Z=0 & N=V / Z=1 or N≠V (Signed Greater/Less Equal)
LO/HS: C=0 / C=1 (Unsigned Lower/Higher Same)
HI/LS: C=1 & Z=0 / C=0 or Z=1 (Unsigned Higher/Lower Same)
Flag Setting Instructions:
CMP: R1 - R2 (result discarded)
TST: R1 & R2 (result discarded)
TEQ: R1 ⊕ R2 (result discarded)
CMN: R1 + R2 (result discarded)

## Slide 20: If-then Statement
C Program | Assembly Program 1 | Assembly Program 2
// a is signed integer if (a < 0 ) { a = 0 – a; } x = x + 1; | ; r1 = a, r2 = x CMP r1, #0 ; Compare a with 0 BGE endif ; Go to endif if a ≥ 0 RSB r1, r1, #0 ; a = - a endif: ADD r2, r2, #1 ; x = x + 1 | ; r1 = a, r2 = x CMP r1, #0 RSBLT r1, r1, #0 ; a = - a if a < 0 ADD r2, r2, #1 ; x = x + 1
C Program | Assembly Program 1 | Assembly Program 2
// a is signed integer if(a <= 20 ¦¦ a >= 25){ x = 1 } | ; r1 = a, r2 = x CMP r1, #20 ; compare a and 20 BLE then ; go to then if a ≤ 20 CMP r1, #25 ; compare a and 25 BLT endif ; go to endif if a < 25 then: MOV r2, #1 ; x = 1 Endif ; implements short circuit evaluation of ¦¦ condition (if 1st condition is true, 2nd condition checking is skipped) | ; r1 = a, r2 = x CMP r1, #20 ; compare a and 20 MOVLE r2, #1 ; a <= 20 → x = 1 CMP r1, #25 ; compare a and 25 MOVGE r2, #1 ; a >= 25 → x = 1 ; else (21 <= a <= 24) → no MOV executed. Does not implement short circuit evaluation. Both conditions will always be evaluated, and r2 is possibly assigned twice. This code only works if the loop body instruction is idempotent, i.e., executing it multiple times gives same result

## Slide 21: If-then-else
C Program | Assembly Program 1
// a is signed integer if (a == 1) x = 3; else x = 4; | ; r1 = a, r2 = b CMP r1, #1 ; compare a and 1 BNE else ; go to else if a ≠ 1 then: MOV r2, #3 ; x = 3 B endif ; go to endif else: MOV r2, #4 ; x = 4 endif:

## Slide 22: For Loop
C Program
int i; //signed int int sum = 0;//signed int for(i = 0; i < 10; i++){ sum += i; }
MOV r0, #0 % sum = 0
MOV r1, #0 % i = 0
loop:
CMP r1, #10 % i < 10 ?
BGE done % exit if i >= 10
ADD r0, r0, r1 % sum += i
ADD r1, r1, #1 % i++
B loop
done: % : is optional after a label
Implementation 1 (Classic compare-and-branch):
C Program (equivalent)
int i = 0; //signed int int sum = 0;//signed int while (i < 10) { sum += i; i++; }
Notes: MOV r0, #0 ; i
MOV r1, #0 ; sum
loop CMP r0, #10 ; check whether i < 10
BGE endloop ; skip if ≥
ADD r1, r1, r0 ; sum += i
ADD r0, r0, #1 ; i++
B loop
endloop

## Slide 23: For Loop
C Program
int i; int sum = 0; for(i = 0; i < 10; i++){ sum += i; }
MOV r0, #0 % sum = 0
MOV r1, #0 % i = 0
B check
loop:
ADD r0, r0, r1 % sum += i
ADD r1, r1, #1 % i++
check: CMP r1, #10 % check whether i < 10
BLT loop % loop if i less than 10.
Implementation 2a:
C Program (equivalent)
int i = 0; int sum = 0; while (i < 10) { sum += i; i++; }

## Slide 24: For Loop
C Program
int i; int sum = 0; for(i = 0; i < 10; i++){ sum += i; }
MOV r0, #0 % sum = 0
MOV r1, #0 % i = 0
%B check deleted
Loop:
ADD r0, r0, r1 % sum += i
ADD r1, r1, #1 % i++
CMP r1, #10 % check whether i < 10
BLT loop % loop if i less than 10.
Implementation 2b:
C Program (equivalent)
int i = 0; int sum = 0; do { sum += i; i++; } while (i < 10);

## Slide 25: Explanations for 2a and 2b
2a and 2b implement two different loop structures:
  Version with “B check” is a pre-test loop (while/for): it tests i < 10 before the first iteration, so the body may execute zero times if the condition is false initially
  Version without “B check” is a post-test loop (do-while): it executes the body once before testing, then repeats while i < 10
Because i starts at 0 and the condition is i < 10, and loop iterates from i=0 to i=9, even though the control-flow order differs.
  If the while condition is initially true (i < 10), program 2b has same behavior as 2a. But if the while condition is initially false (i >= 10), program 2b executes for 1 iteration while program 2a executes for 0 iteration.
Notes: If the initial condition were false, only the pre-test version would skip the loop entirely.

## Slide 26: For Loop
C Program
int i; int sum = 0; for(i = 0; i < 10; i++){ sum += i; }
MOV r0, #0 % sum = 0
MOV r1, #10 % loop count = 10
MOV r2, #0 % i = 0
loop:
ADD r0, r0, r2 % sum += i
ADD r2, r2, #1 % i++
SUBS r1, r1, #1 % --count, set flags
BNE loop % repeat until loop count==0
Implementation 3 (Count-down with SUBS/BNE):
C Program (equivalent)
int sum = 0; // r0 int count = 10; // r1 int i = 0; // r2 while (count != 0) { sum += i; i += 1; count -= 1; }
SUBS r1, r1, #1
Is equivalent to:
SUB r1, r1, #1
CMP r1, #0

## Slide 27: For Loop
C Program
int i; int sum = 0; for(i = 0; i < 10; i++){ sum += i; }
MOV r0, #0 % sum = 0
MOV r1, #0 % i = 0
loop:
CMP r1, #10 % set flags from i-10
ADDLT r0, r0, r1 % if i<10: sum += i
ADDLT r1, r1, #1 % if i<10: i++
BLT loop % if i<10: loop
Implementation 4 (Use conditional execution, i goes from 0 to 9 to execute ADDLT 10 times):
C Program (equivalent)
int i = 0; int sum = 0; while (i < 10) { sum += i; i++; }

## Slide 28: Condition Codes
The possible condition codes are listed below:
    Note AL is the default and does not need to be specified
Not equal
Unsigned higher or same
Unsigned lower
Negative
Equal
Overflow
No overflow
Unsigned higher
Unsigned lower or same
Positive or Zero
Signed Less than
Signed Greater than
Signed Less than or equal
Always
Signed Greater or equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 29: Conditional Execution
Add instruction | Condition | Flag tested
ADDEQ r3, r2, r1 | Add if EQual | Add if Z = 1
ADDNE r3, r2, r1 | Add if Not Equal | Add if Z = 0
ADDHS r3, r2, r1 | Add if Unsigned Higher or Same | Add if C = 1
ADDLO r3, r2, r1 | Add if Unsigned LOwer | Add if C = 0
ADDMI r3, r2, r1 | Add if Minus (Negative) | Add if N = 1
ADDPL r3, r2, r1 | Add if PLus (Positive or Zero) | Add if N = 0
ADDVS r3, r2, r1 | Add if oVerflow Set | Add if V = 1
ADDVC r3, r2, r1 | Add if oVerflow Clear | Add if V = 0
ADDHI r3, r2, r1 | Add if Unsigned HIgher | Add if C = 1 & Z = 0
ADDLS r3, r2, r1 | Add if Unsigned Lower or Same | Add if C = 0 or Z = 1
ADDGE r3, r2, r1 | Add if Signed Greater or Equal | Add if N = V
ADDLT r3, r2, r1 | Add if Signed Less Than | Add if N != V
ADDGT r3, r2, r1 | Add if Signed Greater Than | Add if Z = 0 & N = V
ADDLE r3, r2, r1 | Add if Signed Less than or Equal | Add if Z = 1 or N = !V

## Slide 30: Conditional Execution Examples
C Program | Assembly Program
// a, x are signed integers int32_t a, y if (a <= 0) y = -1; else y = 1; | ; r0 = a, r1 = y CMP r0, #0 MOVLE r1, #-1 ; executed if LE MOVGT r1, #1 ; executed if GT
if(a <= 20 ¦¦ a >= 25){ y = 1; } | CMP r0, #20 ; compare a and 20 MOVLE r1, #1 ; y=1 if less or equal CMP r0, #25 ; CMP if greater than MOVGE r1, #1 ; y=1 if greater or equal
if (a==1 ¦¦ a==7 ¦¦ a==11) y = 1; else y = -1; | CMP r0, #1 CMPNE r0, #7 ; executed if r0 != 1 CMPNE r0, #11 ; executed if r0 != 1 ; and r0 != 7 MOVEQ r1, #1 MOVNE r1, #-1
LE:Signed Less than or Equal
GT:Signed Greater Than
NE: Not Equal
EQ: Equal
Notes: Sequence of conditional instructions:
- no instruction must reset cond code flags
- BL corrupts flags so must be last
- limit sequence to max 3 or so instrs
Can use different condition codes. Give if then else example. Note GCD practical coming later.
Conditional compare
- resets condition code when executed
- compiler will make use of this
- can be difficult for a human to understand!
Not just for compare, using data processing with condition code and S bit is useful in some circumstances.
LDM/LDR instruction cannot set flags due to datapath issues (data comes back only at the very end of the cycle, so there is no opportunity to perform a comparison and set the status flags).
a ⟶ r0
y ⟶ r1

## Slide 31: Thought Experiments
This version (top) does not work, since we cannot use any condition code ?? in MOV?? . CMPGT compares r0 with 25 only if the previous result was >.That already changes the flags set by CMP. So by the time you reach MOV?? r1, #1, the CPU has only one current set of flags, and those flags cannot represent both comparisons at once.
  If we have MOVGE, then if r0 <= 20, then y = 1 should be executed but it is not.
  If we have MOVLE, then if r0 >= 25, then y = 1 should be executed but it is not.
CMP r0, #20 ; compare a and 20
CMPGT r0, #25 ; CMP if greater than
MOVGE r1, #1 ; executed when r0 >= 25
a | CMP r0,#20 result | Does CMPGT r0,#25 run? | Final flags mean | Should y=1? | Is y assigned 1
10 | a < 20 | No | still “less than 20” | Yes | NO
22 | a > 20 | Yes | now “22 < 25” | No | No
27 | a > 20 | Yes | now “27 > 25” | Yes | Yes
if(a <= 20 || a >= 25){
y = 1;
}

## Slide 32
CMP r0, #1
CMP r0, #7
CMP r0, #11
MOVEQ r1, #1
MOVNE r1, #-1
This version (bottom) is incorrect, since only the last “CMP r0, #11” sets the Z flag, overwriting flags set by previous two CMP instructions.

## Slide 33: Explanations for Compound Boolean Expression
Compound condition (a==1 || a==7 || a==11):
  CMP r0, #1
  CMPNE r0, #7 ; executed if r0 != 1
  CMPNE r0, #11 ; executed if r0 != 7
  MOVEQ r1, #1
  MOVNE r1, #-1
CMP r0, #1 compares a with 1 and sets Z=1 if equal, else Z=0.
CMPNE r0, #7 runs only if the previous compare was not equal, and if it runs, it refreshes the flags by comparing a with 7.
CMPNE r0, #11 runs only if a was not 1 and not 7, and if it runs, it compares a with 11 to set Z accordingly.
MOVEQ r1, #1 executes only when Z=1 from any of the comparisons, so y becomes 1 if a matched 1, 7, or 11.
MOVNE r1, #-1 executes only when Z=0 after all relevant compares, so y becomes -1 when none of the values matched.

## Slide 34: Conditional Execution Examples Con’t
C Program | Assembly Program w/ Branching | Assembly Program w/ Conditional Execution
int32_t x, y; …… if (x + y < 0) x = 0; else x = 1; | % r0 = x, r1 = y ADDS r0, r0, r1 BPL PosOrZ MOV r0, #0 B done PosOrZ MOV r0, #1 done %Could use BGE if you assign negative r1 to r2, then SUBS r0, r0, r2 | ADDS r0, r0, r1 MOVMI r0, #0 ;return 0 if N = 1 MOVPL r0, #1 ;return 1 if N = 0
uint32_t x, y; …… while (x != y) { if (x > y) x = x – y; else y = y – x; } | gcd CMP r0, r1 BEQ end ; if x = y, done BLO less ; x < y SUB r0, r0, r1 ; x = x – y B gcd less SUB r1, r1, r0 ; y = y – x B gcd End | gcd CMP r0, r1 SUBHI r0, r0, r1 SUBLO r1, r1, r0 BNE gcd
Notes: BPL PosOrZ: Branch to PosOrZ if condition PL is true (N == 0 indicating Positive or Zero) for ADDS r0, r0, r1
MOVPL r0, #1: conditional move that executes only when condition PL is true
MOVMI r0, #0: conditional move that executes only when condition MI (N == 1 indicating Negative) is true

## Slide 35: Combination
Except that it does not change the status flags, CBZ R1,label is equivalent to:
  CMP R1, #0
  BEQ label
Except that it does not change the status flags, CBNZ R1,label is equivalent to:
  CMP R1, #0
  BNE label
Instruction | Operands | Brief description
CBZ | R1, label | Compare and Branch if Zero
CBNZ | R1, label | Compare and Branch if Non Zero

## Slide 36: Break vs. Continue
Example code for break | Example code for continue
for(int i = 0; i < 5; i++){ if (i == 2) break; printf(“%d, ”, i) } | for(int i = 0; i < 5; i++){ if (i == 2) continue; printf(“%d, ”, i) }
Output: 0, 1 | Output: 0, 1, 3, 4

## Slide 37: Break Example
C Program | Assembly Program 1 | Assembly Program 2
// Find string length char str[] = "hello"; int len = 0; for( ; ; ) { if (*str == '\0') break; str++; len++; } | ;r0 = string memory address ;r1 = string length ADR r0, str MOV r1, #0 Loop: LDRB r2, [r0] CBNZ r2, notZero B endloop notZero: ADD r0, r0, #1 ; str++ ; to let r0 point to the next char, since each char is 1 byte (would increment by 4 for integer array) ADD r1, r1, #1 ; len++ B loop endloop: | ;r0 = string memory address ;r1 = string length ADR r0, str MOV r1, #0 Loop: LDRB r2, [r0] CBZ r2, endloop ADD r0, r0, #1 ADD r1, r1, #1 B loop endloop:
Option 1: Uses CBNZ (Compare and Branch if Non-Zero) to branch to the loop body, falling through to B endloop if the value is zero.
Option 2: Uses CBZ (Compare and Branch if Zero) to branch immediately to the end if the terminator is found, skipping the loop body.

## Slide 38: Continue Example
C Program | Assembly Program 3
// Count characters that are not 'l' until the null terminator char *str = "hello"; int count = 0; for ( ; *str != '\0'; str++) { if (*str == 'l') { continue; } count++; } | ; r0 = string address (str) ; r1 = count = 0 ADR r0, str MOV r1, #0 Loop: LDRB r2, [r0] CBZ r2, endloop ; if '\0' => break CMP r2, #’l’ ; if char == 'l' BEQ contLoop ; continue and skip count++ ADD r1, r1, #1 ; count++ contLoop: ADD r0, r0, #1 ; str++ B loop endloop:

## Slide 39: IT (If-Then) instruction
On smaller ARM cores (Cortex-M0), not all data instructions support condition suffixes directly; instead you must use an IT instruction (Thumb-2) or branches.
"IT" (If-Then) instruction in the ARM Thumb-2 instruction set (16 bits) allows conditional execution of up to four instructions based on a condition flag (like EQ, NE, etc.).
IT{x{y{z}}} {cond}, where x, y, and z specify the existence of the optional second, third, and fourth conditional instruction respectively. x, y, and z are either T (Then) or E (Else). T = execute the following instruction if condition is True; E = execute the following instruction if condition is False
  IT — 1 following instruction (If)
  ITT — 2 following instructions (If-Then)
  ITE — 2 following instructions (If-Else)
  ITTE, ITEEE, etc. — up to 4 instructions total
ITTE NE ; If-Then-Then-Else
ANDNE r0,r0,r1 ; executed if Not Equal
ADDNE r2,r2,#1 ; executed if Not Equal
MOVEQ r2,r3 ; executed if Equal
ITT AL ; AL (Always) condition executes two 16-bit instructions unconditionally; the last ADD is outside the IT block.
ADDAL r0,r0,r1 ; 16-bit ADD, not ADDS
SUBAL r2,r2,#1 ; 16-bit SUB, not SUB
ADD r0,r0,r1 ; expands into 32-bit ADD, and is not in IT block
ITT EQ ; Executes both instructions only if Equal condition is true
MOVEQ r0,r1
BEQ dloop ; branch at end of IT block is permitted
ITT EQ ; Executes both instructions only if Equal condition is true
MOVEQ r0,r1
ADDEQ r0,r0,#1
You do not need to write IT instructions in your code.
The assembler generates them for you automatically according to the conditions specified.
Notes: You do not need to write IT instructions in your code.
The assembler generates them for you automatically according to the conditions specified.

## Slide 40: Summary: Condition Codes
    Note AL is the default and does not need to be specified
Not Equal
Unsigned Higher or Same
Unsigned LOwer
MInus (Negative)
EQual
oVerflow Set
oVerflow Cleared
Unsigned HIgher
Unsigned Lower or Same
PLus (Positive or Zero)
Signed Less Than
Signed Greater Than
Signed Less than or Equal
ALways
Signed Greater or Equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N!=V
Notes:     Condition codes are simply a way of testing the ALU status flags.
    Note AL is the default and does not need to be specified

## Slide 41: Summary: Branch Instructions
 | Instruction | Description | Flags tested
Unconditional Branch | B label | Branch to label | 
Conditional Branch | BEQ label | Branch if EQual | Z = 1
 | BNE label | Branch if Not Equal | Z = 0
 | BCS/BHS label | Branch if unsigned Higher or Same | C = 1
 | BCC/BLO label | Branch if unsigned LOwer | C = 0
 | BMI label | Branch if MInus (Negative) | N = 1
 | BPL label | Branch if PLus (Positive or Zero) | N = 0
 | BVS label | Branch if oVerflow Set | V = 1
 | BVC label | Branch if oVerflow Clear | V = 0
 | BHI label | Branch if unsigned HIgher | C = 1 & Z = 0
 | BLS label | Branch if unsigned Lower or Same | C = 0 or Z = 1
 | BGE label | Branch if signed Greater or Equal | N = V
 | BLT label | Branch if signed Less Than | N != V
 | BGT label | Branch if signed Greater Than | Z = 0 & N = V
 | BLE label | Branch if signed Less than or Equal | Z = 1 or N = !V

## Slide 42: Summary: Conditionally Executed
Add instruction | Condition | Flag tested
ADDEQ r3, r2, r1 | Add if EQual | Add if Z = 1
ADDNE r3, r2, r1 | Add if Not Equal | Add if Z = 0
ADDHS r3, r2, r1 | Add if Unsigned Higher or Same | Add if C = 1
ADDLO r3, r2, r1 | Add if Unsigned LOwer | Add if C = 0
ADDMI r3, r2, r1 | Add if Minus (Negative) | Add if N = 1
ADDPL r3, r2, r1 | Add if PLus (Positive or Zero) | Add if N = 0
ADDVS r3, r2, r1 | Add if oVerflow Set | Add if V = 1
ADDVC r3, r2, r1 | Add if oVerflow Clear | Add if V = 0
ADDHI r3, r2, r1 | Add if Unsigned HIgher | Add if C = 1 & Z = 0
ADDLS r3, r2, r1 | Add if Unsigned Lower or Same | Add if C = 0 or Z = 1
ADDGE r3, r2, r1 | Add if Signed Greater or Equal | Add if N = V
ADDLT r3, r2, r1 | Add if Signed Less Than | Add if N != V
ADDGT r3, r2, r1 | Add if Signed Greater Than | Add if Z = 0 & N = V
ADDLE r3, r2, r1 | Add if Signed Less than or Equal | Add if Z = 1 or N = !V

## Slide 43: Summary: Condition Codes
Condition Codes:
  EQ/NE: Z=1 / Z=0 (Equal/Not Equal)
  LT/GE: N≠V / N=V (Signed Less Than/Greater Equal)
  GT/LE: Z=0 & N=V / Z=1 or N≠V (Signed Greater/Less Equal)
  LO/HS: C=0 / C=1 (Unsigned Lower/Higher Same)
  HI/LS: C=1 & Z=0 / C=0 or Z=1 (Unsigned Higher/Lower Same)
Flag Setting Instructions:
  CMP: R1 - R2 (result discarded)
  TST: R1 & R2 (result discarded)
  TEQ: R1 ⊕ R2 (result discarded)
  CMN: R1 + R2 (result discarded)

## Slide 44: References
Lecture 27. Branch instructions
  https://www.youtube.com/watch?v=_QKD7f1cmRI&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=27
Lecture 28. Conditional Execution
  https://www.youtube.com/watch?v=9hlxG8L5-G4&list=PLRJhV4hUhIymmp5CCeIFPyxbknsdcXCc8&index=28